## Slide 1: Chapter 1
Introduction to Networks

## Slide 2: What is a Network
Anytime you connect two or more systems together, you have a network
Printer
Host
Host
Notes: Hosts talk to each other in something in a language known as “binary”
Binary is a bunch of 1s and 0s

## Slide 3: Network Terms
Workstations
  Beefy desktops – think CAD machines
Servers
  Power horses that provide specific services to the network
  Examples
    Mail
    File
    Web
Hosts
  Anything that connects to a network
Notes: End-users usually use workstations
Workstations are more powerful and run more than one CPU
Servers tend to be job-specific, really good at their jobs
Hosts are any network device with an IP address

## Slide 4: What is a Local Area Network (LAN)
Hub
Switch
Servers
Servers
Printer
Marketing
Sales
A local area network (LAN) is usually restricted to spanning a particular geographic location
Notes: Your home is a LAN. It is the combination of all you devices being connected and being able to communicate with one another
The way this is setup, Marketing can access its own resources and servers, Sales can access its own resources and servers as well
Marketing and Sales, based on this graphic are no able to connect to the other’s resources without a router

## Slide 5: Wide Area Networks (WANs)
Servers
Internet
Corp
Branch2
Branch1
Usually need a router
Span geographical locations
Usually slower than a LAN
Can use public or private media
Distributed
  A lot of different computers in different areas
Centralized
  Central computer remote computers connect to
  Remote offices to central office
Notes: Collection of Local Area Networks (2 or more)
The internet is a WAN (the largest)
Usually operated and managed by a service provider like Verizon, AT&T
Routers are the key to connecting different LANs to each other
Distributed is the internet; millions of users in different places that are all interconnected accessing resources on the web
An example of centralized is remote workers logging into their company owned computers and being able to have access to the company’s network and resources from their own home

## Slide 6: Multi-Protocol Label Switching (MPLS)
MPLS Network Logical Connections Between Sites
Corporate Office
Branch Offices
Each router assigns labels to data when the data heads toward the MPLS cloud
MPLS is a switching mechanism that imposes labels (numbers) to data and then uses those labels to forward data when the data arrives at the MPLS network .
Notes: MPLS allows you to create a private link between different sites
Usually done through a ISP (internet service provider)
The best thing about this is speed, Quality of Service, and interface independent
Interface independent means all your networks could communicate regardless of the type of connection they have (DSL, Fiber, etc)
You can add labels to each packet traversing the network
Traditionally your router sent data and made decisions of where to send data based on its IP address
MPLS allows the router to put a 32-bit label on your data, which would make your data reach its destination quicker

## Slide 7: Peer-to-Peer vs Client-to-server
Peer to Peer
  Think direct connection
Client Server
  Internet today
Notes: Peer-to-Peer networks is when you connect one client to another client
A client being a computer, they have a direct connection.
Internet is not needed
Client-to-server networks are when there is 1 or more computers connecting to one or more servers that hold all the services and resources
When you go to google.com your client is talking to the web server that has google’s web application running on it

## Slide 8: Peer-to-Peer Networking
Hub
Hub
Users | Password | Access
Mickey | !Tails? | Full
Pluto | $NoKats | Read
Louie | ^Wet#! | Read
Users | Password | Access
Millie | #Shorts? | Read
Pluto | &LittleTail! | Full
Louie | ^Wet#! | Full
Users | Password | Access
Millie | #Shorts? | Read
Mickey | My!Ears? | Read
Louie | ^Wet#! | Full
Users | Password | Access
Millie | #Shorts? | Read
Pluto | &LittleTail! | Full
Mickey | &&Boss!@ | Full
Millie
Mickey
Pluto
Louie
  Think direct connection
Notes: In order for each computer to get resources, it must speak directly to the computer it needs resources from

## Slide 9: Client Server Networks
Hub
Hub
Users | Password | Access
Millie | #Shorts? | Read
Pluto | &LittleTail! | Full
Louie | ^Wet#! | Full
Mickey | --Earls? | Write
Millie
Mickey
Pluto
Louie
Server
Notes: In the Client-server network, everyone is pulling resources the server, the server holds and manages all resources

## Slide 10: Physical Topologies
Here is a list of the various topologies you’re most likely to run in to these days:
  Bus
  Star
  Ring
  Mesh
  Point-to-point
  Point-to-multipoint
  Hybrid
Notes: You need to learn the differences among all these topologies

## Slide 11: Bus Topology
Server S1
Laser Printer
Advantages
  Easy to install
  Not expensive
  Minimal Cabling
Disadvantages
  Difficult to troubleshoot
  Difficult to change
  Difficult to move
  No fault tolerance
Notes: Every thing is connected via ONE cable
Single-point of failure
If the network goes down, it is hard to figure out how or why

## Slide 12: Star Topology
Hub
Advantages
  Moving or adding stations is easy
  A single failure will not break network
  Easy to troubleshoot
Disadvantages
  Higher cost to install
  Has a single point of failure
Notes: Also known as Hub-and-Spoke
All devices are connected to one centralized device, instead of one cable
This also has a single-point of failure, can somebody tell me where that is?
Much easier to expand out using this topology

## Slide 13: Ring Topology
Similar to a Bus Topology
Notes: Basically the same as the Bus topology
Not very common anymore primarily because it has a single-point of failure

## Slide 14: Mesh Topology
n(n-1)/2
Robust Fault tolerance
Very costly
Notes: Imagine having to connect each computer directly to every computer
So lets say you have 20 computers, how many connections would you need?
You’d need 190 connections
This one has fault tolerance, but it comes at a very high price
Very rare to see this topology

## Slide 15: Other Topologies
Point to Point
Point to Multi-point
Hybrid Topologies
Serial Connection, Like a T1 between Routers
Branch Offices
Corporate Office
Notes: Point-to-point is a direct connection between 2 routers or switches
Remember the way these objects look, all these items are representative of routers
A link between a computer and a switch or a hub is also considered a point-to-point connection
Point-to-multipoint is when each router is part of the same network
A hybrid topology is simply a combination of two or more different physical or logical network topologies operating within the same network
Think of the word “logical” like virtual. They are interchangeable

## Slide 16: Backbones and Segments
Marketing
Sales
Segments
Backbone
Notes: The backbone of a network is like your spine, if your spine is damaged you cannot operate normally
This is the main line that all your devices and segments are connected to
Segments are the lines that connect your devices on your network to the backbone