## Slide 1: Chapter 12
Wireless Networking

## Slide 2: Cellular Technology
Global System Mobile – GSM
  SIM Chip holding all the information abut the subscriber
  Subject to cloning
  AT&T an T-Mobile
Code Division Multiple Access – CDMA
  Uses a unique code for each call and spreads the data across the spectrum
  Sprint and Verizon
Notes: GSM: cell phone that contains a SIM card, allows you to move your SIM card from phone-to-phone
Used multiplexing which allowed multiple users to communicate to one tower over the single set of frequencies
CDMA: everyone communicates at the same time using a specific code, codes were used to filter each call on the receiving end

## Slide 3: Wireless Technology
802.11 Standard from IEEE
  802.11a – 5GHz
  802.11b – 2.4GHz
  802.11g – 2.4GHz
  802.11n – 2.4GHz/5GHz
  802.11ac – 5GHz
  802.11ax – 2.4GHz/5GHz
Notes: 802.11ax: Uses both 2.4 and 5 GHz
Enables more than 35% speed burst
Reduces overhead and latency

## Slide 4
Notes: Pay attention to the frequencies, data speeds

## Slide 5: Wireless Terminology
Wireless Access Point (WAP)
Wireless Network Interface Card (WNIC)
Independent Basic Service Set (IBSS) – Ad Hoc Network
Basic Service Set
Wireless Controller/Wireless Distribution System(WDS)
Mobile Hot Spot

## Slide 6: Wireless Access Points
Wireless networks have a component connecting all wireless devices together, the device is known as a wireless access point (WAP), or just AP.
Wireless access points have at least one antenna (sometimes two for better reception—called diversity) and a port to connect them to a wired network.
Antenna
  Omni-Directional-Point to multi-point
  Directional (Yagi)- Point to point
Notes: Connects all wireless devices together
Can operate as a repeater, switch, or router depending on how its implemented
Has at least one antenna
Antennas act as both transmitters and receivers
Talk about the difference with the antenna directions
Directional antennas usually provide greater range than Omni-directional
The MAC address for the AP is called a BSSID: Basic Service Set Identifier

## Slide 7: Wireless Network Interface Card (Wireless NIC)
A wireless NIC does the same job as a traditional NIC; but instead of having a socket to plug some cable into, the wireless NIC has a radio antenna.
Notes: Does the same job as a traditional NIC, but it has a radio antenna

## Slide 8: Wireless Networks
In ad-hoc mode, the wireless devices communicate directly WITHOUT the need for an access point.
An example of this is two laptops with wireless NICs installed. If both cards were set up to operate in ad-hoc mode, they could connect and transfer files as long as the other network settings, like protocols, were set up to enable this as well.
  This is an independent basic service set (IBSS)
Ad-Hoc Mode: Independent Basic Service Set (IBSS)
Notes: In this mode, the wireless NICs can communicate directly using 802.11 WITHOUT an AP
All you need is two wireless NICs and two computers
Bring the computers within 90-100m of each other
Cannot scale out well and is not recommended

## Slide 9
Access point
Internet
DS*
Wireless clients
Wireless Networks
Infrastructure Mode: Basic Service Set (BSS)
Notes: NICs communicate only with an AP instead of directly w/ each other
All comms go through the AP
Wireless clients appear to the rest of the network as it would on a standard wired host

## Slide 10: Wireless Networks
Infrastructure Mode: Extended Service Set (ESS)
SSID Sales
Channel 1
Channel 6
LAN Backbone
SSID Sales
Overlapping
20%
Wireless clients
Wireless clients
“Wireless Cell”
“Wireless Cell”
Notes: Set multiple access points to the same SSID and mobile wireless clients can roam around freely within the same network.
This creates an Extended Service Set ( ESS)) and provides more coverage then a single access point.
For users to be able to roam throughout the wireless network from AP to AP without losing their connection to the network, all APs must overlap by at least 10% of their signal.

## Slide 11
Standalone and controller-based
Notes: In a stand alone solution, all the APs have a full OS loaded, running, and each must be managed separately
In the controller-based system, the APs do not have a full OS running on them
The controller and AP split duties; can be called thin APs
When an AP has a full OS it is referred to as a thick AP

## Slide 12
Figure 12.15 Mobile Hotspot
Notes: Can connect your laptop, tablet, media devices, or any gaming device to the Internet at decent speeds
You can also use your phone as a mobile hotspot

## Slide 13: Internet of Things (IOT)
What is IOT
Bluetooth
  BlueJacking
  BlueSnarfing
Near Field Communication (NFC)
Infrared (IR)
Notes: Refrigerators, alarm systems, thermostats, etc
BlueJacking: transmits data to the target device
BlueSnarfing: high jacking Bluetooth signals to steal information
NFC: tap to pay
IR: Tv remote

## Slide 14: Implementing WIFI
Placement
Channels
  Free channels are 1, 6, 11
Password
  WEP
  WPA
  WPA2
Notes: Try to use non-overlapping channels to decrease interference and latency
Different encryption tools to secure your network
WEP had extreme vulnerabilities so don’t ever use it
WPA came after and was ended to be a temporary fix until a new successor was created
WPA2 uses CCMP Block Cipher Mode; provides data confidentiality with AES encryption
WPA3 uses GCMP Block Cipher Mode; stronger encryption than WPA2

## Slide 15: Wireless Security
Rogue Aps
Denial of Service (DOS)
War Driving
War Chalking
Notes: Rogue APs: AP’s that connect to your wired infrastructure without your knowledge
Wardriving: involves attackers searching for wireless networks with vulnerabilities while moving around an area in a moving vehicle
Warchalking: is the drawing of symbols in public places to advertise an open Wi-Fi network