## Slide 1: Chapter 13
Using STATISTICS AND SENSORS to ensure network availability

## Slide 2: Performance metrics/sensors
Device/Chassis
  Temperature
    Overheating a main cause of reboots
    PC usually cools itself with fans but may require additional cooling (liquid)
    Dust is a major cause of overheating
  CPU
    We use counters to monitor the CPU
      Processor\% Processor time
        Time CPU spends executing and non-idle thread
        Should not exceed 85%
      Processor\% User time
        Time spent doing work for an application
        Should not exceed baseline
      Processor\% Interrupt time
        Time spent servicing hardware interrupts
        Should not be over 15%
      System\Processor Queue Length
        Number of threads in queue
        Should not exceed number of CPU’s
Notes: Temperature: can be an early sign of overutilization or hardware issues
This is important to monitor, so that you can keep your devices and servers running w/ optimal performance
Overheating will usually send your computer into constant rebooting
Make sure to clean your fan
Do not obstruct air flow into your computer
CPU Usage: is the metric to determine how hard your device is working
Use vendor documentation in how to counteract issues with CPU

## Slide 3: Performance metrics/sensors
  Memory
    Memory\% Committed Bytes in Use
      Virtual memory in use
      >80% more memory is required
    Memory\Available Mbytes
      Physical memory available
      <5% more memory is required
    Memory\Free System Page Table Entries
      Number of entries not in use
      <5000 may have a memory leak
    Memory\Pool Non-Paged Bytes
      The size of objects that cannot be paged to the disk
      >175MB may have a memory leak
    Memory\Pool paged Bytes
      Size of objects that can be paged
      >250MB may have memory leak
    Memory\Pages per Second
      Writing and read rate during paging
      >1000 may be a memory leak
Notes: Make sure to have enough memory because once a device reaches its capacity, it usually can no longer operate
Consult the vendor for specific documentation or information for specific services in relation to memory issues

## Slide 4: Performance metrics/sensors
Network Metrics
  Bandwidth
    Network Interface\Bytes Total\Sec
      NIC capability currently in use
      >70% - interface is saturated
    Network Interface\Output Queue Length
      Packets in the output queue
      >2- NIC is not keeping up
  Latency
    Consistent delay in traffic
    Measured in Round Trip Time (RTT)
  Jitter
    Variance in delay
Notes: Make sure to keep an eye on your bandwidth, if you exceed your bandwidth your network will suffer miserably
Latency: is the wait time between request and response
Everybody hates latency and slow internet right? Monitor it
Best way to monitor all these metrics is to grab a baseline when you first start working at a company
It is easier to troubleshoot issues when they can be identified early on
Jitter: the time between frames, when phone calls are choppy
These metrics showing issues can be an indication of malware on your devices or operating on your network

## Slide 5: Interface Statistics/status
Link State
  Is it up or down
  First ting to check if we get a link error
Speed/Duplex
  Both ends should match
  Run the ‘ show running configuration command’ (sh run) to check interfaces on routers and switches
  Usually set to Auto
Send/Receive Traffic
  To check on interface you would run ‘ sh int <int>’
Cyclic Redundancy Checks (CRCs)
  Error detection mechanism
Protocol Packet and Byte counts
  To check you would run ‘sh int <int>
Notes: First determine if the router and switch is operational
Use device manager to verify speed and duplex settings on a Windows device
CRC: When these errors occur, something has corrupted the received packet

## Slide 6: Interface Errors or Alerts
CRC Errors
  Damaged packet
    Bad port, bad cable, duplex mismatch, etc
Giants
  Packets that exceed the maximum packet size and/or incorrect frame check sequence
  Usually discarded
  Caused by a bad NIC
Runts
  Packets that do not meet minimum packet size
  Usually discarded
  Caused by bad NIC
Encapsulation Errors
  Missing header from OSI layer
  Example- layer 3 missing layer 2 information. Cant forward
Notes: CRC errors: can be caused by a faulty port on the device or a bad ethernet cable
Giants: packets that are discarded because they exceed the maximum packet size of the medium
Runts: packets that are discarded because they don’t meet the minimum packet size requirements
Encapsulation Error occurs when a header from the OSI layer is missing; switches are expecting different frames

## Slide 7: SNMP
Ports 161 and 162
3 Versions
  Version 3 should be used. 1 and 2 are unsecure and deprecated
Traps
  Uses a Network management System to communicate with devices
  Uses a GET message to query devices
  Devices will send a trap when a problem occurs
Object Identifiers(OIDs)
  Standardized mechanism to name objects or things with a globally unambiguous persistent name
  In SNMP each node in a management information base (MIB) is identified by an OID
Management Information Bases (MIBs)
  A hierarchical structure of OID’s
Notes: Simple Network Management Protocol operates using Ports 161 and 162
Version 3 has message integrity checks, encryption, and authentication
It gathers data from devices on the network from a management station at fixed or random intervals
It records a baseline
It can be utilized as a watch dog to notify an administrator of events or sudden alarms
OIDs: are the stats gathered from network devices
MIB: a database of data

## Slide 8: Environmental factors and sensors
Temperature
Humidity
Electrical
  UPS
  Multiple Circuits
Flooding
  Severs/datacenters on upper floors or raised floors
Notes: Server rooms or infrastructure rooms including routers, switches, etc should be in a cool room provided with a high powered HVAC system and proper ventilation
Humidity cant be to damp or too dry
Too dry causes static electricity
Too damp causes connections to corrode or shorts to occur
50% is the magic number of humidity
Make sure there are devices in those rooms/buildings to monitor these metrics

## Slide 9
Notes: Server rooms and data centers should be located on upper floors or have raised floors

## Slide 10: Misc
Baselines
Netflow data
Uptime/downtime
  99.99
  99.999
Notes: NetFlow: allows you to gather traffic statistics from all traffic flows and share the data over multiple devices
It has a probe and a collector, the probe sits out on the network collecting information and it sends the summary reports to the collector
Uptime/Downtime: status page to know if certain devices are up or down