## Slide 1: Chapter 2
OSI Model
Notes: It is crucial for you to understand the OSI model, it helps in troubleshooting
It is an industry standard
Everyone will talk about Layer 2 or Layer 3 issues

## Slide 2: OSI Model
(Open Systems Interconnection model) A standard means of describing network communication by defining it as a series of layers, each with specific input and output.
Application
7
Presentation
6
Session
5
Transport
4
Network
3
Data Link
2
Physical
1
Albums
All
Producing
People
Stop
Seem
To
To
Needs
Need
Daddy
Domino’s
Puff
Pizza
Notes: This is the reference model of how communications should take place
Here are a couple mnemonics to help you remember the order of the OSI layers
The layers are hierarchical; organized in an order

## Slide 3: OSI Layer Functions
Application | File, print, message, database, and application services
Presentation | Data encryption, compression, and translation services
Session | Dialog control
Transport | End-to-end connection
Network | Routing
Data Link | Framing
Physical | Physical topology
Notes: Divided into two groups
Top 3 layers is what the end-user is able to see
The bottom 4 layers is how data transmits from one place to another

## Slide 4: The Upper Layers
Application | Provides a user interface
Presentation | Presents data Handles processing such as encryption
Session | Keeps different applications’ data separate
Transport | 
Network | 
Data Link | 
Physical | 
Notes: Users interact with the Application layer: google.com is what you see on your computer screen
The upper layers are responsible for applications communicating between computers(hosts)

## Slide 5: The Lower Layers
Application | 
Presentation | 
Session | 
Transport | Provides reliable or unreliable delivery Performs error correction before retransmit
Network | Provides logical addressing which routers use for path determination
Data Link | Combines packets into bytes and bytes into frames Provides access to media using MAC address Performs error detection not correction
Physical | Moves bits between devices Specifies voltage, wire speed, and pin-out of cables
Notes: The bottom layers define how data transfers through switches, routers, etc

## Slide 6: Application Layer- Layer 7
The layer we see
Protocols operating at this level:
  HTTP
  FTP
  DHCP
  POP3
Notes: This is the layer where you interact with the computer or a website
This is NOT talking about an actual app
It’s more about how something would be applied
There would be a web browser for the application of HTTP
There would be an email program for the application of SMTP
It acts as an interface between application programs
Like learning your ABC’s will lead to you learning how to read

## Slide 7: Presentation Layer-Layer 6
Character encoding
Application encryption
Often combined with the Application Layer
Protocols operating at this layer
  TLS (Transport Layer Security)
  SSL (Secure Socket Layer )
Notes: At this layer, it presents data to the Application layer and is responsible for data translation and code formatting
Performs data compression, decompression, encryption, and decryption
Ensures that two different system’s application layers are able to understand each other

## Slide 8: Session Layer-Layer 5
Communication management between devices
  Start, stop, restart
Half-duplex, full-duplex
Control protocols, tunneling protocols
Protocols operating at this layer:
  NetBIOS
  SMB
Notes: Provides communication between two hosts
Bridging the network layers to the software layers
Simplex(one direction)
Half-duplex(one direction at a time)
Full-duplex(bi-directional)
Allows multiple web browser sessions on your computer at the same time

## Slide 9: Transport Layer- Layer 4
Transmission Control Protocol (TCP)
  3-way Handshake
  Flow Control
  Windowing
  Acknowledgements
User Data-Gram Protocol (UDP)
Notes: TCP vs UDP
Connection-oriented vs connectionless
UDP is not reliable. It is when you send a text and hope it gets delivered (like sending a text from an iPhone to an Android) – joke
TCP has far more security involved in its delivery
The connection established in TCP is known as a virtual circuit

## Slide 10: A Connection Oriented Session
Sender
Receiver
SYN
SYN/ACK
ACK
Connection Established
Data transfer
(Send bytes of Segments)
Notes: This is the 3-way Handshake
Sender sends a SYN message, both hosts also agree on how much data will be sent in either direction
Receiver sends back its own SYN message along with an ACK message
Sender responds back with an ACK message
Thereby establishing a connection for data to be transferred
If at any point the 3-way handshake breaks, the data will not be sent
“Hello, are you there?”
“Yes, are you there?”
“Yes”
Data gets sent

## Slide 11: Flow Control
Sender
Receiver
Buffer full
Not ready – STOP!
Segments processed
GO!
Transmit
Notes: Flow control gives the receiver of information authority to determine how much data will be sent by the sender
All data that is sent has to be confirmed that it was received
Any data that was “dropped” is automatically resent
Data is placed in the proper order
A manageable flow of data is maintained to not overwhelm the system, which would lead to data loss
A buffer happens when one host receives too much data at once and it has to place the extra data in a memory bank
The receiver will send out a message saying “Hold up, give me a second”
Data will stop, receiver will catch up, and then ask for the rest of the data to be sent

## Slide 12: Acknowledgements
Sender
Receiver
Receive 1
Window size of 1
Receive 2
Ack 1
Ack 2
Send 1
Send 2
Window size of 3
Ack 4
Send 1
Send 2
Send 3
Send 4
Notes: Guarantees data wasn’t duplicated or lost
The sender sends data in segments
It waits for the ACK message from the receiver before it sends its next segment of data
The sender sets a timer, if time runs out before it receives an ACK, the sender sends the data again

## Slide 13: Network Layer- Layer 3
The “routing” layer
Internet Protocol (IP)
Unit of measure at this layer is packets
  Data Packets
  Router update packets
Routers operate at this layer
Maintain Route tables- Directions to other networks
Protocols operating at this layer:
  NAT
  ICMP
Notes: Transports data between devices that aren’t local
Routers and “Layer 3 switches” operate at this level
Packet gets received and it checks the destination IP address
Where is this package supposed to be delivered
The router looks in its contacts (routing table) for the destination IP address
Once it finds the destination, it sends it to that router, “drops the package off”
If the router can’t find the destination, the packet gets dropped or lost
Two types of packets: data packets and router updates
An example of a data packet protocol is IP or IPv6
Route update packets help to build and maintain routing tables on each router
An example is the yelp or google maps; keeps updated where business or things are located

## Slide 14: Data Layer- Layer 2
The basic network “language”
  The foundation of communication at the data link layer
Data Link Control (DLC) protocols
  MAC (Media Access Control) address on Ethernet
  LLC (Logical Link Control) ID Network Layer protocols
The “switching” layer
Switches operate at this layer
Unit of measure at this layer is Frame
Protocols operating at this layer:
  ARP
  NDP
Notes: Ensures that messages are delivered to the proper device on a LAN using the MAC addresses
It also translates messages from the Network layer into bits for the Physical layer to transmit
Adds a data frame to a message, which contains the destination and sender/receiver hardware address
Facilitates communication between devices on a LAN
Devices that operate at this level are NICs, a bridge, a switch, or a WAP
MAC: physical addressing is defined here

## Slide 15: Physical Layer- Layer 1
The physics of the network
  Signaling, cabling, connectors
  This layer isn’t about protocols
You have a physical layer problem.”
  Fix your cabling, punch-downs, etc.
  Run loopback tests, test/replace cables, swap adapter cards
  Hubs operate at this layer
Notes: Sends and receives bits. 1s and 0s
Physical cables (copper or fiber optic cables)
It specifies the physical topology, physical interface (punch-down blocks)
Repeaters and Hubs

## Slide 16: Encapsulation/De-Encapsulation
Application
7
Presentation
6
Session
5
Transport
4
Network
3
Data Link
2
Physical
1
Application
7
Presentation
6
Session
5
Transport
4
Network
3
Data Link
2
Physical
1
Notes: When data transmits across a network to another device encapsulation and decapsulation occurs
Encapsulation is placing a header at each level it goes up the OSI model
The layers only communicate with the layer above and below itself
Headers allow that to occur smoothly
Decapsulation is removing headers at each level going down the OSI model to strip the segment to receive the data

## Slide 17: Data Encapsulation
Upper layer data
Upper layer data
TCP Header
Segment
IP Header
Packet
LLC Header
Packet
MAC Header
FCS
FCS
0101110101001000010
Application
Presentation
Session
Physical
Transport
Network
Data Link
Segment
Packet
Frame
Bits
PDU
Notes: Encapsulation starts at the Application layer and moves down
At layer 7 it adds a protocol (HTTP, FTP, SMTP, etc)
At layer 6 it adds how the data is encoded
At layer 5 it decides how the connection will be managed
At layer 4 it adds whether it is connection-oriented or connection less
At layer 3 it adds IP addresses, usually destination addresses
At layer 2 it adds MAC addresses
At layer 1 it adds the actual binary data that is being sent