## Slide 1: Chapter 21
Data Center Architecture and Cloud Concepts

## Slide 2: Three-tiered
Core
  Provides interconnectivity between all network pods in the data center
Distribution/aggregation
  Provide redundant connection, connect to the core, and implement security, access control and layer 3 routing
Access/edge
  Devices attach to the network
Notes: Core: the center of the network; web servers, databases, and applications
Many people need access to this layer
Distribution Layer: midpoint between the core and the users; manages the path of the network to the users. COMMUNICATION BETWEEN SWITCHES
Access/Edge: where the users are located; workstations and printers

## Slide 3: Traffic Flows
North-South
  Refers to traffic entering and leaving the data center
East-West
  Traffic that flows inside the data center between devices
Notes: North-South traffic is entering or leaving the data center
East-West is traffic and data that is being sent between devices within the data center

## Slide 4: Software-defined Networking
Network devices are managed as complete set and not individually from a central controller
  Application Layer
    Standard network applications like IDS/IPS, load balancers, proxy servers, etc
    Explicitly or programmatically communicate to the SDN Controller
  Control layer
    Management Plane
    Processes configuration, monitoring, and other application-specific information between the application and infrastructure layers
  Infrastructure Layer
    Forwarding Plan
    Consists of network hardware controlling the forwarding and processing for the network
    Collects network health information
Notes: SDN: combines the functionality of data, control, and management to one centralized device or controller
Takes all the different functions of different devices and combines them into one to operate separately logically
Application layer: includes firewalls, IDS/IPS, Load balancers
Control layer: acts as the SDN controller, manages the traffic flow
Infrastructure layer: made up of the physical switches and routers

## Slide 5: Spine and Leaf
  Datacenters are evolving to a two-tier architecture
  The two-tier architecture offers the following advantages over the traditional three tier designs.
    Resiliency
      Each leaf switch connects to every spine switch
    Latency
      Ultra low
      Maximum 2 hops over a high-speed network for east-west traffic
    Performance
      Active-active up-links allow traffic to flow over the least congested available link
    Scalability
      Easy to add leaf switches for port capacity and spine switches for uplinks
    Adaptability
      Multiple networks are often managed from SDN controllers
Notes: Each leaf switch connects to each spine switch
Leaf switches and spine switches don’t connect directly to each other

## Slide 6
  Top-rack switching
    Place access switches at the top of the rack
    Connects to distribution or spine and leaf with high-speed links from 10G up to 100G
    Advantage is lower-cost copper or coaxial cable is used and confined to the rack
Notes: Top-rack switching: each leaf switch is on top of a physical network rack
Good for cabling, its redundant, and fast. When adding to your network its costly

## Slide 7: Storage Area Networks
Separate private network of storage devices
Connection Types
  Fiber Channel over Ethernet (FCoE)
    Encapsulates fiber channel frames within ethernet frames
    Allows traffic on the IP network
  Fiber Channel
    Used to connect computer data storage
    2, 4, 8, 16Gbps
    Not compatible with the regular IP based data network
  Internet Small Computer Systems Interface (iSCSI)
    IP-based standard method for encapsulating SCSI commands within IP Packets
    Can use the same network for storage and data
Notes: SAN: high-capacity storage devices that are connected by a high-speed private network separate from the LAN
Data collection, data management, and the use of data
Very efficient at reading and writing
Block-level access so if you have a large file, you can rewrite part of the data without having to overwrite the entire file
Requires a lot of bandwidth, usually has it own network
Fibre Channel: Allows you to connect servers and storage together at very high speeds
You need a Fibre channel switch
FCoE: If you don’t have a Fibre channel interface on a server, usually integrates with an existing Fibre channel infrastructure
Not routable
iSCSI: Makes a remote disk, look and operate like a local disk; can be managed in software instead of hardware

## Slide 8: Branch Office vs. on-premises datacenter vs co-location
Deciding to where to place a datacenter can be a daunting task.
Do I want it closer to the user, do I want to build and manage a datacenter or do I want to lease space
Branch Office
  Puts data closest to the user.
  No remote links
On premise
  Separate datacenter that has its own staff
  Can be resilient to environmental considerations(backup Datacenter)
Co-location
  Provider builds out datacenter and leases space

## Slide 9: Cloud Deployment Models
Public Cloud
Providers deploy infrastructure and then make it accessible to any customers who wish to take advantage of it in a multitenant model
Private Cloud
Used to describe any cloud infrastructure that is provisioned for use by a single customer
Community Cloud
Run in a multitenant environment, but the tenants are limited to members of a specifically designed community
Hybrid Cloud
A catch-all term used to describe cloud deployments that blend public, private, and/or community cloud services together

## Slide 10: Service Models
IaaS – Infrastructure as a Service
  Building blocks for IT
  Network, Compute, Storage
  Very Flexible
PaaS – Platform as a Service
  No need to manage underlying infrastructure
  Focus on deployment and management
SaaS – Software as a Service
  Ran and managed by the service provider

## Slide 11: Infrastructure as Code
Process of automating the provisioning, management, and deprovisioning of infrastructure services through scripted code rather than human intervention.
The major advantages to using an IaC approach
  Increasing the reusability of code
  Reducing the time spent by operations team creating infrastructure components
  Increasing the speed of infrastructure creation
  Reducing the likelihood of configuration errors by leveraging common templates
Notes: You use coding to build the infrastructure of your servers, routers, and networks
When you make updates, you just update the code
You can use the same code to make multiple instances of the same application, switch, or router
Copy-paste-create
AUTOMATE EVERYTHING!

## Slide 12
The breakdown of responsibility across multiple cloud models

## Slide 13
Connectivity Options
  VPN
  Direct Connect
Multitenancy
Elasticity
Scalability
Notes: Direct Connect: a dedicated circuit can be ordered and installed between your data center and an interconnection provider or directly to the cloud company