## Slide 1: Chapter 22
ensuring network availability

## Slide 2: Performance metrics
Device/Chassis
  Temperature
    Overheating a main cause of reboots
    PC usually cools itself with fans but may require additional cooling (liquid)
    Dust is a major cause of overheating
  CPU
    We should use as much of the CPU cycles as possible- you paid for it
    However, there is a line you don’t want to cross
    CPU over 90% we start having problems
    We use counters to monitor the CPU- discussed in chapter 13
  Memory
    Can be as severe as high CPU utilization and can be an indicator of malware
    Can result in the system crashes and /or performance degradation
    We can use monitoring tools to monitor the memory utilization and send alarms
    Discussed in Chapter 13

## Slide 3: Performance metrics/sensors
Network Metrics
  Bandwidth
    Water of Life for the network
    You can never have enough
    A great deal of time is spent monitoring and trying to improve bandwidth
  Latency
    Consistent delay in traffic
    Measured in Round Trip Time (RTT)
  Jitter
    Variance in delay

## Slide 4: SNMP
Ports ?
3 Versions
  Version 3 should be used. 1 and 2 are unsecure and depricated
Traps
  Uses a Network management System to communicate with devices
  Uses a GET message to query devices
  Devices will send a trap when a problem occurs
Object Identifiers(OIDs)
  Standardized mechanism to name objects or things with a globally unambiguous persistent name
  In SNMP each node in a management information base (MIB) is identified by an OID
Management Information Bases (MIBs)
  An heiarchial structure of OID’s

## Slide 5: SNMP Traps

## Slide 6: Network device logs
Log Review
  Traffic Logs
    Network Devices
  Audit Logs
    Windows/linux systems
  Syslog
  SiEM
Logging Levels/Severity Levels

## Slide 7: Cisco Log Levels

## Slide 8: Interface Statistics/status
Link State
  Is it up or down
  First ting to check if we get a link error
Speed/Duplex
  Both ends should match
  Run the ‘ show running configuration command’ (sh run) to check interfaces on routers and switches
  Usually set to Auto
Send/Receive Traffic
  To check on interface you would run ‘ sh int <int>’
Cyclic Redundancy Checks (CRCs)
  Error detection mechanism
Protocol Packet and Byte counts
  To check you would run ‘sh int <int>

## Slide 9: Interface Errors or Alerts
CRC Errors
  Damaged packet
    Bad port, bad cable, duplex mismatch, etc
Giants
  Packets that exceed the maximum packet size and/or incorrect frame check sequence
  Usually discarded
  Caused by a bad NIC
Runts
  Packets that do not meet minimum packet size
  Usually discarded
  Caused by bad NIC
Encapsulation Errors
  Missing header from OSI layer
  Example- layer 3 missing layer 2 information. Cant forward

## Slide 10: Environmental factors and sensors
Temperature
Humidity
Electrical
  UPS
  Multiple Circuits
Flooding
  Severs/datacenters on upper floors or raised floors

## Slide 12: Misc
Baselines
Netflow data
Uptime/downtime
  99.99
  99.999