## Slide 1: Chapter 23
Cable connectivity issues and tools

## Slide 2
Specifications and Limitations
  Throughput
    Capabilities are ever increasing
    AWS datacenters operate at petabyte speeds
  Speed Distance
    Higher speeds are more sensitive to distance
    Optical cable have overcome this but are very expensive
Cable considerations
  Shielded vs Unshielded
    Both are twisted pair cables to reduce the effects of crosstalk and noise
    Shielded adds a layer of foil or mesh shielding to protect against electromagnetic interference
  Plenum and riser-rated
    Used inside buildings
    Plenum are fire resistant and have low fume emittance and can be use din air ducts
    Riser cables are cheaper and can be used to run between floors that don’t traverse air ducts
Cable Application
  Rollover/console cable
  Crossover Cable
  Power over Ethernet
Notes: Rollover cable: reverse the pin out on the other end
Crossover cable: Like devices; T568A + T568B

## Slide 3
Common issues
  Attenuation
  Interference
    EMI/RFI
  Decibel (dB) loss
    Measure of signal loss
    To much loss end to end may cause link failure
  Incorrect pinout
  Bad ports
  Open/short
    Physical fault in the cable
Notes: Attenuation: 100m distance meaning the closer you are to that 100m, the more your signal degrades
dB: how much of the transmission is lost in transit to its destination (UPC vs APC)
Bad ports can lead to CRC errors

## Slide 4
Common issues
  Light emitting diode (LED) status indicators
  Incorrect transceivers
    Convert signals from devices to cabling requirements-
  Duplexing issues
  Transmit and received (TX/RX) reversed
  Dirty optical cables
  Bent Pins
  Split Pairs
    Wire pairs connected to the wrong pair on the other end
Notes: Dirty Optical cables: dirty fiber optic cables

## Slide 5: Hardware Tools
Cable Testers
  Cable-testing tools can range from simple, inexpensive mechanical devices to elaborate electronic testers that automatically supply you with test results.
An inexpensive cable tester

## Slide 6: Loopback Plug
A loopback test is a diagnostic procedure in which a signal is transmitted and returned to the sending device after passing through all or a portion of a network or circuit.

## Slide 7: Hardware Tools
Wire-Map Testers
  A wire-map tester is a device that transmits signals through each wire in a copper twisted-pair cable to determine if it’s connected to the correct pin at the other end.
Continuity Testers
  A continuity tester is an even simpler and less expensive device than a wire-map tester that’s designed to check a copper cable connection for basic installation problems like opens, shorts, and crossed pairs.

## Slide 8: Hardware Tools
Protocol Analyzer
  A protocol analyzer is often confused with a packet sniffer because some products really are both.
  A packet sniffer looks at all traffic on a network segment.
  A protocol analyzer analyzes protocols.
Certifiers
  Certification testers or certifiers are used to determine whether your network meets specific International Organization for Standardization (ISO) or TIA standards.
Notes: Protocol analyzer: Wire-shark

## Slide 9: Hardware Tools
Time-Domain Reflectometer (TDR)
  A time-domain reflectometer (TDR) is a tool that finds and describes faults in metallic cables like twisted wire pairs and coaxial cables.
Optical Time-Domain Reflectometer (OTDR)
  An optical time-domain reflectometer (OTDR) is an optoelectronic instrument used to give you information about optical fibers.
We use OTDRs to give us information about the following:
The fiber’s estimated length
Its overall attenuation
The location of faults
Notes: TDR finds faults in twisted wire pairs and coaxial cables
OTDR: same thing, but for fiber

## Slide 10: Hardware Tools
Multimeter
  A multimeter or a multitester (also called a volt/ohm meter [VOM]) is a multitasking electronic measuring instrument.
  Used to troubleshoot electrical problems in a wide array of electrical devices like batteries, motor controls, appliances, power supplies, and wiring

## Slide 11: Hardware Tools
Toner Probe
  A toner probe, also called a tone generator, is a simple copper cable tester that is simple to use and can be used to trace a wire in a wall.

## Slide 12: Hardware Tools
Butt Set
  A butt set is essentially a portable telephone that allows you to test and monitor analog lines.
Punch-Down Tool
  Twisted-pair cable usually terminated in wiring closets using a tool known as a punch-down tool.

## Slide 13: Hardware Tools
Crimper
  A wire crimper, often simply called crimper, is a handy tool found in most network technicians’ tool bags.
  Crimpers are primarily used for attaching ends onto different types of network cables via a process known as crimping.
Cable Stripper/Snips
  Before you can crimp a connector onto the end of a wire, you have to strip the cable with a type of cable stripper (or snips) and then properly put the wires into the connector.

## Slide 14: Hardware Tools
Fiber Light Meter
  Measure receives levels and wavelengths to verify cable is working
Fiber Fusion Splicer
  Used to repair fiber cables
  Minimizes light scattering or being reflected back in the cable