## Slide 1: Chapter 7
IP Addressing

## Slide 2: IP Terminology
Bit
Byte (8 bits)
Octet (8 bits)
Network Address
IP Address
  IPv4 or IPv6
Broadcast Address
Notes: Bit: Binary digit of 1 or a 0
Byte: usually 8 bits
Octet: made up of 8 bits
Network address: A logical or physical address to uniquely identify a host or device on a network
Broadcast address: used by applications and hosts to send information to all hosts on the network

## Slide 3: IPv4
Uses Dotted Decimal Notation
4 sets of Octets
Total of 32 bits
Example: 192.168.9.35

## Slide 4: Public IP Addresses
Class A
  IP addresses that start from 1 to 126
  /8 Subnet Mask
Class B
  IP addresses that start from 128 to 191
  /16 Subnet Mask
Class C
  IP address that start from 192 to 223
  /24 Subnet Mask
Class D – IP addresses from 224 – 239
Class E – IP addresses from 240 - 255
Notes: Class A, the first byte is assigned to the network address and the 3 remaining bytes are used for the host addresses
Class B, the first 2 bytes are assigned to the network address and the remaining 2 bytes are used for host addresses
Class C. the first 3 bytes of a Class C network address are dedicated to the network address and the final byte is for the host address
Class D is used for multicast addresses
Class E is used for scientific purposes

## Slide 5: Private IP Address
Class A
  Anything from 10.0.0.0 to 10.255.255.255
Class B
  Anything from 172.16.0.0 to 172.31.255.255
Class C
  Anything from 192.168.0.0 to 192.168.255.255
Loopback address: 127.0.0.1
Automatic Private IP Addressing (APIPA)
  Anything from 169.254.0.0 to 169.254.255.255
Notes: Private IP addresses can be used on a private network, but they are not routable through the internet
This is helpful so we never run out of unusable IP addresses
We use something called Network Address Translation, which allows us to have multiple private IP addresses on the network, but when we send data out through our router, the destination IP address can only see our public IP address

## Slide 6: Message types
Unicast: one-to-one
Broadcast: one-to-all (NOT used in IPv6)
Multicast: one-to-many-of-many (specific)
Anycast: one-to-one-of-many
Notes: Unicast: Sending packets to a single destination
Multicast: Packets sent from a single source and transmitted to many devices on different networks (one-to-many)
Broadcast: Sent to all hosts on the network
Anycast: Multiple destination devices will have the same anycast address; allows a device to send a request and the closest device with that anycast address will respond
13 Root DNS servers, but there are thousands of DNS servers configured with anycast addresses so your device can reach the closest one to your geographic location

## Slide 7: IPv6
Uses Hexadecimal Notation
8 sets of 4 hexadecimal numbers
128 Bits
Shorten Zeros
Notes: Next-generation IP
The more time goes by, the more people and more devices that utilize the internet
Shortened Expression rules:
1. Drop any leading zeros in each individual block
2. You can remove consecutive zeros and replace them with a double colon, but you can only do this ONCE

## Slide 8: IPv6 Shorten Expression Rules
Step 1. Drop any leading zeros in each individual block
Step 2. You can remove consecutive zeros and replace them with a double colon, but you can only do this ONCE
  2001:0db8:3c4d:0012:0000:0000:1234:56ab
  Step 1 | 2001:db8:3c4d:12:0:0:1234:56ab
  Step 2 | 2001:db8:3c4d:12::1234:56ab

## Slide 9: IPv6 Types of Addresses
Unicast – Direct one to one message
Global Unicast – Public IP
Link-Local Address – APIPA
Unique Local Address – Private IP
Multicast – One to many
AnyCast – One to Group

## Slide 10: IPv6 Special Addresses
::1 Loopback address
2000:: Global Unicast Range
FC00:: Unique Local Range
FE80:: Link Local Address
FF00:: Multicast Address

## Slide 11: Other IPv6 Terms
DualStacking – Router is able to route IPv4 and IPv6 traffic
6to4 tunneling: useful for carrying IPv6 packets over a network that’s still running on IPv4
  Teredo: Tunnels IPv6 through NATed Ipv4 (Microsoft implementation)
  Miredo is Linux Implementation
Notes: Allows our devices to communicate over the network or the internet over IPv4 or IPv6
6to4: useful for carrying IPv6 packets over a network that’s still running on IPv4
It takes an IPv6 packet and slaps an IPv4 header in front of it
NAT breaks the tunnel encapsulation, so you have to be able to modify the packets to be received
Teredo disguises your tunnel traffic into UDP packets
Miredo is used on IPv6 Linux or Unix machines to communicate on the IPv4 directly without a dual-stack router or the 6to4 tunneling (rarely used)