## Slide 1: Chapter 8
Subnetting and Routing

## Slide 2: Subnetting
Will be covered separately

## Slide 3: Troubleshooting IP Adresses
Troubleshooting IP addressing is obviously an important skill because running into trouble somewhere along the way is pretty much a sure thing, and it’s going to happen to you. Here are the steps:
  Open a DOS window, and ping 127.0.0.1.
  From the DOS window, ping the IP address of the local host.
  From the DOS window, ping the default gateway (router).
  If steps 1 through 3 were successful, try to ping the remote server.
  If the user still can’t communicate with the server after steps 1 through 4 are successful, you probably have some type of name resolution problem and need to check your Domain Name System (DNS) settings.
Notes: Give your work scenario

## Slide 4: Command Line Tools
Packet InterNet Groper (ping)
  Uses an Internet Control Message Protocol (ICMP) echo request and replies to test if a host IP stack is initialized and alive on the network.
traceroute
  Displays the list of routers on a path to a network destination by using TTL time-outs and ICMP error messages. This command will not work from a DOS prompt.
tracert
  Same command as traceroute, but it’s a Microsoft Windows command and will not work on other devices, like a Cisco router or Unix box.
arp -a
  Displays IP-to-MAC-address mappings on a Windows PC.
ipconfig /all
  Used only from a DOS prompt. Shows you the PC network configuration.
Notes: Ping: echo request and replies to test if an device is alive on the network
Traceroute: List the routers on a path to a network destination using TTL and ICMP error messages
Works on a router, MAC, or Linux
Tracert: same thing but used for Windows
Arp –a: Displays IP-to-MAC address mappings on PC
Ipconfig/all: shows your entire network configuration of your device

## Slide 5: Network Address Translation
What is Network Address Translation?
Overloading/Port Address Translation (PAT)
Notes: NAT: Allows you to have multiple private IP addresses linked to 1 public IP address
Overloading: Most popular; mapping many unregistered IP addresses to one single IP address by using different ports
You can have thousands of users to connect to the internet using only one public IP address

## Slide 6: NaT Names
Inside Local – Your Private IP (address before translation)
Outside Local – Private IP of the Destination (before translation)
Inside Global – Your Public IP (address after translation)
Outside Global – Public IP of destination (after translation)

## Slide 7: How NAT works

## Slide 8: How PAT works (NAT Overloading)
Host B
63.41.7.3
DA
170.168.2.2
SA
170.168.2.2
DA
10.1.1.1
SA
10.1.1.1
Protocol 10.1.1.1 | Inside Local IP Addresses: Port | Inside Global IP Addresses: Port | Outside Global IP Addresses: Port
TCP | 10.1.1.3:1492 | 170.168.2.2:1492 | 63.41.7.3:23
TCP | 10.1.1.2:1723 | 170.168.2.2:1723 | 63.41.7.3:23
TCP | 10.1.1.1:1024 | 170.168.2.2:1024 | 63.40.7.3:23
NAT Table
Inside
10.1.1.1
10.1.1.2
10.1.1.3
Host C
63.40.7.3
DA
170.168.2.2
Internet